## Slide 1: Portraying the Earth
Chapter 2

## Slide 2: The Nature of Maps
How and why do we describe the earth using maps?
When we need to understand the world around us we use maps.
A map is a two or three-dimensional representation of the Earth and a spatial distribution of selected phenomena– normally the components of a landscape.
The basic attributes of a map
  Show direction, distance, size, and shape
    Spatial relationships of features of the earth
Maps have a special purpose

## Slide 4: Map Scale
The scale of a map gives the relationship between length measured on the map and corresponding actual distance on the ground.
Scale types
  Graphic Map Scale uses a line marked off in graduated distances.
  Fractional Map Scale compares map distance with ground distance in a proportional fraction or ratio called a representative fraction.
  Verbal Map Scale or word scale, state in words the ratio of the map scale length to the actual distance on the Earth’s surface.

## Slide 5: Large Scale and Small Scale
Large Scale Maps.
  Large representative fraction, or the denominator is small. 1:10,000
  See more detail in the map
  Portrays a smaller area of the earth
Small Scale Maps
  Small representative fraction, or the denominator is large, 1:1,000,000
  See less detail in the map
  Portrays a large area of the earth

## Slide 6: Large Scale Map

## Slide 7: Small Scale Map

## Slide 8: Map Essentials - Components of a Map
Title: short brief summary of map’s contents
Date: should be the date of the compilation of the data found on the map.
  Can also be the date of the data found on the map
Legend: information about the symbols colors, and such used to depict the features of the map
Scale: if map is more than a pictogram. Scale can be either graphic, verbal, for fractional.

## Slide 9: Components of a Map
ht://www.eventrite.com/event/7649380503?utm_source=Members&utm_campaign=39381712db-2011_11_09_Meeting_Announcement10_18_2011&utm_medium=email&utm_term=0_cf57194600-39381712db-283093897

## Slide 10: Map Essentials
Direction: a north arrow (top of the map, should be north). If there is a grid, there should still be a north arrow.
Location: grid, such as latitude and longitude, to be used to locate features
Data Source: source of the data found on the map
Projection type: in what projection is the data on the map

## Slide 11: Globes
Best substitute for depicting the earth
The only thing changed in depicting the earth onto a globe is the size
Shows comparative distances, sizes, and accurate directions.
Represents without distortion, the spatial relationships of features of the earth
Problem, because the globe will be set a very small scale (detail is lost)

## Slide 12: Map Projections
A system whereby the spherical surface of the earth is transformed to display on a flat surface.
Three basic projection styles for the earth
  Cylinder
  Cone
  Flat
Using a globe inside the Earth with each style, the lines or features are transferred to the paper

## Slide 14: Equivalence versus Conformaty
Equivalence Projection – equal area projection
  The size ratio of any area on the map to the corresponding area on the ground is the same all over the map
  Desirable because misleading impressions are avoided.
  Difficulty to achieve on small-scale maps, to maintain proper areal relationships

## Slide 15: Equivalence versus Conformaty
Conformal Projection – conformal relations
  Proper angular relationships are maintained so that the shape of something on the map is the same as its shape on the Earth
  Meridians and Parallels cross each other at right angles.
  Most notable projection is probably the Mercator projection.
  A Robinson projection is a compromise between a equivalence and conformality.

## Slide 16: Projections
Mercator, the most famous Projection
  Developed in 1569 by Flemish geography and cartographer, Gerhardus Mercator.
  Developed for use in navigation of ships
  Advantage: shows Loxodromes or Rhumb lines as straight lines.
  Problem with the Mercator,
    Extreme East-West distortion in higher latitudes
    To compensate Mercator stretched the spacing north and south to compensate.
    Allowed shapes to be reasonably accurate but proper size relationships distorted.

## Slide 17: Projections
The Plane projection – azimuthal or zenithal projection.
  Obtained by projecting markings of the globe on a flat piece of paper that is tangent to one point of the globe
  Used often in large scale maps or small areas of the globes
  Usually is shown from either the North Pole or the South Pole

## Slide 18: Projections
The Conic Projection
  Obtained by projecting the markings of the globe onto a cone wrapped tangent to or intersecting a portion of the globe
  Normally the apex of the cone is positioned about a pole which means the circle of tangency coincides with a parallel.
  Best suited for regions of east-west orientation in the mid latitudes.

## Slide 20: Funky Projections
Pseudocylindrical projection – elliptical or oval projection
  Football shape of usually the whole world
Interrupted projections
  Most famous – Goode’s interrupted homolosine projection

## Slide 22: Computer Cartography
Using computers to create maps
  Symap (first software used to make maps
    1965
  Global Positioning Systems
  Remote Sensing
  Imagery
  Multi-spectral Remote Sensing
  Geographic Information Systems
Widely used today
Expanding industry

## Slide 23: Isolines
Portray the spatial distribution of some phenomenon on the earth.
  Isarithm, isogram, isopleth, and isometric lines are synonymous for our purposes
  Most important to physical geography
    Elevation Contour Line – depicts elevation
    Isotherm – depicts equal temperature
    Isobar – depicts equal atmospheric pressure
    Isohyet – depicts equal quantities of precipitation
    Isogonic Line – depicts equal magnetic declination

## Slide 24: Characteristics of Isolines
Always closed lines- is line comes to the end of a map the line probably proceeds to the next area
Represent gradations in quantity, never touch or cross one another
Numerical difference between one isoline and another is an interval.
Isolines close together indicate a steep gradient, those far apart indicate a gentle gradient.

## Slide 25: Global Positioning System (GPS)
A satellite based system for determining accurate positions on or near the Earth’s surface.
Developed in the 1970’s for the military
Based on 24 high-altitude satellites configured so that a minimum of 4 satellites are in view of any position on the Earth.
Each satellite continuously transmits both identification and positioning information that can be picked up by receivers on Earth.
Position determined through triangulation.

## Slide 26: Remote Sensing
Any measurement or acquisition of information by a recording devise that is not in physical contact with the object under study-in this case the Earth.
  Satellite remote sensing
    Imagery obtained from geosynchronous orbit satellites.
  Aerial Photographs
    Photographs taken from an elevated platform, such as a balloon, airplane or rocket.
    Photographs classified either oblique or vertical.

## Slide 27: Imagery
Orthophoto Maps – multicolored, distortion-free photographic image maps.
  All displacement caused by camera tilt or differences is removed.
  Shows greater detail than a conventional map but retains the characteristic of a map
Color or Near Infrared Imagery
  Refers to the visible-light region of the electromagnetic spectrum
  Near Infrared Color is used to depict vegetation
Thermal Infrared Sensing – depicts temperature

## Slide 28: Multi-spectral Remote Sensing
Multi-spectral or Multi-band – different regions of the electromagnetic spectrum
  Landsat imagery
    Launched in the 1970’s and 1980’s
      Four spectral bands
Earth Observing System (EOS)
  Moderate Resolution Imagery Spectroradiometer (MODIS)
    36 spectral bands
Radar and Sonar Sensing

## Slide 29: Geographic Information Systems (GIS)
Automated system for the capture, storage, retrieval, analysis, and display of spatial data.
A GIS can manipulate rows and columns of tabular and links it to the spatial features it represents.
All the features depicted in the GIS have a coordinate system that ties them to a coordinate system of the earth
  Knows where it is on the earth’s surface
Allows for the many layers of different features to be over-laid to form maps that can be used to make decisions.